## Slide 1
SPOOKY
The QUBO Mathematical Model
Formulation, extensions beyond the paper, empirical weight tuning, the binary-encoding dead end, and what a task-allocation layer would add.
Javier González Villasmil · arXiv:2602.14799

## Slide 2
AGENDA
What this deck covers
01
QUBO, not ILP→QUBO
why the model is native QUBO from the start
02
Core penalties
one-hot, adjacency, start/goal, lock — as in the paper
03
Extra penalties
backtracking, teleportation, approximation heuristics
04
Collision model
crash penalty, and swap-collision (not in the paper)
05
Weight tuning
why it's empirical, and the current production values
06
Binary vs one-hot
the encoding explored on a branch — and why it lost
07
Task allocation
the layer this system does not yet have
Spooky — QUBO Mathematical Model · Agenda
2

## Slide 3
01
QUBO, Not ILP → QUBO
Spooky's model was never an integer/binary linear program that got compiled down. It is authored directly as a QUBO — that distinction shapes everything after it.
Spooky — QUBO Mathematical Model · QUBO, Not ILP → QUBO
3

## Slide 4
MODELING PHILOSOPHY
The standard pipeline vs. Spooky's pipeline
Standard OR practice
Model as ILP / BLP:
min cᵀx s.t. Ax ≤ b, x ∈ {0,1}ⁿ
Constraints are hard, explicit inequalities/equalities
Compile down to QUBO for a quantum/annealing solver:
add slack variables for every inequality
pick big-M penalty weights from a provable bound
flatten equalities into quadratic penalty terms
QUBO is a compilation target — a solver adapter, not the model
Spooky
Model directly as a QUBO:
C(x) = Σₖ λₖ Pₖ(x)
No intermediate ILP layer, no slack variables, no big-M
Every requirement is authored as a quadratic penalty term
one-hot, adjacency, start/goal, crash, swap, …
Objective and “constraints” are the same mathematical object
Penalty weights (λ) are first-class, tuned directly —
not derived from a worst-case bound
Spooky — QUBO Mathematical Model · QUBO, not ILP→QUBO
4

## Slide 5
WHY IT MATTERS
Big-M vs. tuned penalties
Big-M conversion picks weights from a worst-case algebraic bound — mathematically safe, but it produces a poorly conditioned Q matrix (huge dynamic range between terms).
A poorly conditioned Q matrix is exactly what breaks annealers and QAOA: dominant terms drown out weaker ones, and normalization can no longer rescue every term at once.
Because Spooky's penalties are authored (not derived), each λ can be tuned against the solver's actual behavior — what the paper calls the empirical tuning process (Section 5).
This also makes the unconstrained nature of QUBO an asset rather than a workaround: the “constraints” were never anything but penalty terms to begin with.
Spooky — QUBO Mathematical Model · QUBO, not ILP→QUBO
5

## Slide 6
BACKGROUND
QUBO: the core definition
C(x) = xTQx
x ∈ {0,1}ⁿ — binary decision variables
Q ∈ ℝⁿˣⁿ — symmetric / upper-triangular, encodes pairwise relations
Unconstrained: every requirement is embedded in the cost function
Diagonal of Q = linear terms • off-diagonal = quadratic (pairwise) terms
Since xⱼ = xⱼ² for binary variables, linear terms fold onto the diagonal — everything becomes one quadratic form
Equivalent to the Ising model (x → {−1,+1}) — the bridge to annealing / QAOA Hamiltonians
Objective = weighted penalty sum
F(x) = λ₁·distance(x) + λ₂·obstacle(x) + …
The QUBO is not solved directly — it's converted into a Hamiltonian and solved via quantum annealing, QAOA, or classical simulated annealing. Spooky targets all three through the same builder → solver interface (DWave_solver.py, Pennylane_solver.py).
Spooky — QUBO Mathematical Model · QUBO background
6

## Slide 7
BACKGROUND
Variable encoding — grid & graph
Grid (linear one-hot)
idx = robot·(M·N·T) + t·(M·N) + i·N + j
Graph (node-based)
idx = robot·(nodes·T) + t·nodes + nodeid
Groups variables per timestep, enumerated in standard reading order (grid) or node index (graph)
Multi-robot uses a global clock: robot 1 gets M·N·T slots, robot 2 the next M·N·T, and so on — linear index growth in the number of robots
Local per-robot time is offset relative to the first active robot, so collision penalties only need to compare robots active at the same absolute timestep
This exact index formula is what every penalty term below derives its variable indices from — any new constraint has to follow it
Spooky — QUBO Mathematical Model · Variable encoding
7

## Slide 8
02
Core Constraint Penalties
The four penalties every valid QUBO path needs, plus goal-lock — straight from the paper's formulation section.
Spooky — QUBO Mathematical Model · Core Constraint Penalties
8

## Slide 9
CORE PENALTY · 1 OF 4
One-hotness — exactly one cell per timestep
Phot = Khot · Σt=0T (1 − Σi,j xi,j,t)²
A physical agent occupies exactly one position at any given time — this penalty drives the QUBO toward that reality.
Expanding the square shows the origin of every cross-term xᵢxⱼ in Q: (Σx)² = Σx² + 2Σᵢ<ⱼ xᵢxⱼ
Interacts strongly with the adjacency penalty below — the two frequently need post-processing to resolve disagreements (see the Continuity check, later in the paper).

## Slide 10
CORE PENALTY · 2 OF 4
Adjacency — no teleporting between cells
Padj = Kadj · Σt=0T−1 Σi,j xi,j,t·(1 − Σ(k,l)∈N(i,j) xk,l,t+1)
N(i,j) is the 4-connectivity neighbor set of cell (i,j) — the most computationally expensive penalty, best precomputed into a neighbor dictionary.
Obstacle avoidance is handled structurally here, not as its own penalty: obstacle cells are simply removed from every N(i,j), so a move into one already breaks adjacency.
Same trick applies to graphs — unconnected nodes are never in each other's neighbor set, so no separate obstacle logic is needed there either.

## Slide 11
CORE PENALTY · 3 OF 4
Start & goal conditions
Pstart = −Kstart · xsi,sj,0
Pgoal = −Kgoal · xei,ej,T (naïve, last-step-only form)
Both reduce from a squared form (1 − x)² to a linear reward once x² = x is used for binary variables — same simplification as one-hotness.
The naïve goal penalty only rewards reaching the goal at the exact final timestep, which assumes you already know T. In production this is replaced by the late-time weighted version (next section) — same idea, applied at every step with growing weight.
Goal cannot be rewarded at t = 0, or it directly conflicts with the start-condition penalty.

## Slide 12
CORE PENALTY · 4 OF 4
Goal lock — stay once you arrive
Plock = Klock · Σt=0T−2 xg,t·(1 − xg,t+1)
Classical planners never worry about this — they don't operate on fixed timesteps. QUBO does, and it doesn't inherently know the right time window, so it tends to keep moving past the goal unless told to stop.
Not treated as essential: extra post-goal moves can simply be clipped from the decoded path instead. In practice this penalty can be dropped without much cost.

## Slide 13
03
Extra Penalties & Heuristics
Not required for a valid path, but required for a good one — these fix teleportation, backtracking, and windowed goal-seeking.
Spooky — QUBO Mathematical Model · Extra Penalties & Heuristics
13

## Slide 14
EXTRA PENALTY
Backtracking — punish revisiting cells
Pbt = Kbt · Σ(i,j)≠goal Σt₁<t₂ xi,j,t₁·xi,j,t₂
A global constraint (not per-timestep): penalizes any pair t₁ < t₂ where the agent occupies the same non-goal cell twice.
A backtracking solution is, by construction, never optimal — this steers the solver toward the direct path and away from wandering near the start or goal.
Explicitly excludes the goal cell, or it would conflict with the goal-lock penalty above.

## Slide 15
EXTRA PENALTY
Teleportation penalty & distance heuristics
Teleportation penalty (K_tp): penalizes reaching the goal earlier than physically possible, using the Manhattan/Euclidean lower bound on step count — balances the goal penalty and meaningfully improves results in practice.
Grid — Manhattan distance
d = |x₂ − x₁| + |y₂ − y₁|
Graph — Euclidean distance
d = √((x − xgoal)² + (y − ygoal)²)
Any valid path needs at least the Manhattan/Euclidean number of steps — fewer means the answer is invalid, more can be encouraged to shrink toward it.
Spooky — QUBO Mathematical Model · Extra penalties
15

## Slide 16
EXTRA PENALTY
Windowed goal-seeking: late-time & approximation penalties
Late-time goal penalty
Weight on reaching the goal increases every timestep (up to ~2×) instead of firing only at the last step
Fixes the constant-time approach's teleportation problem and the early-time approach's over-eagerness — empirically the most effective of the three
Approximation penalty (K_goal_approx)
Used inside a time window that can't reach the goal yet — rewards approaching it (shrinking Manhattan/Euclidean distance) instead
Paired with an obstacle potential field so the solver favors open space, not just “closer” cells — also spreads multi-robot traffic away from clutter
Must stay weak relative to backtracking, or it fights the windows that already tried and failed to reduce distance
Spooky — QUBO Mathematical Model · Extra penalties
16

## Slide 17
04
Multi-Robot Collision Model
Crash avoidance is in the paper. Swap-collision isn't — it's flagged there as a known limitation, but it's already implemented.
Spooky — QUBO Mathematical Model · Multi-Robot Collision Model
17

## Slide 18
COLLISION · IN THE PAPER
Crash penalty — same cell, same time
Pcrash = Kcrash · Σt Σr₁<r₂ Σ(i,j)∈shared xr₁,i,j,t·xr₂,i,j,t
Only evaluated over cells both robots can actually reach at time t (shared_cells) — keeps the penalty term count small instead of scanning the whole grid.
Rule of thumb from the config: K_crash must stay ≤ K_adj, or the solver has no incentive to prefer a legal move over sitting through a collision.

## Slide 19
COLLISION · NOT IN THE PAPER
Swap-collision penalty
Pswap = Kcrash·xr₁,txr₂,t + Kswap·(xr₁,t+1xr₂,t + xr₁,txr₂,t+1)
The paper's own Limitations section calls swap-collision out as unsolved: an exact swap detector is quartic (degree 4), not quadratic — QUBO's native degree.
Implemented anyway (QUBOBuilder.apply_swap_penalty / GraphQUBO equivalent) as a pairwise quadratic approximation instead of an exact quartic term:
same-cell/same-time term reuses K_crash unchanged, so base crash protection isn't diluted
two cross-time terms catch robot 1 arriving where robot 2 just was, and vice versa — the actual swap signature
Known over-constraint: the cross-time terms also fire when one robot simply follows another into a just-vacated cell — not a real collision. K_swap is the knob to relax if that false-positive cost outweighs the benefit.
When K_swap is active it replaces the plain crash penalty entirely (build() drops “crash” from the constraint list) so the same-time term is never double-counted.
Spooky — QUBO Mathematical Model · Swap-collision
19

## Slide 20
05
Weight Tuning
Every K constant above is empirical. There's no closed-form optimum — here's the methodology and the current production values.
Spooky — QUBO Mathematical Model · Weight Tuning
20

## Slide 21
METHODOLOGY
Why tuning is empirical, not derived
Unlike big-M in a classical ILP→QUBO conversion — which has a provable bound formula — there is no mathematically “correct” weight for a penalty that was authored, not derived.
Tuning discipline: fit weights against the most general / least constrained scenario first (the open map, fewest active constraints). Fitting to a constrained scenario instead tends to overfit — the solver has more freedom in the general case, so weights that hold there generalize; ones that only work under heavy constraints usually don't.
Normalization scale is the one global knob that keeps weights problem-size-independent: you tune a single number instead of re-deriving every K per map size.
PennyLane / QAOA: scale 2.0 below ~60–100 variables, scale 1.0 above
D-Wave annealing: benefits from a higher scale (5.0) — fewer reads needed for the same or better accuracy
Combined with the time-window approach, this means the main remaining tuning surface is just “how many timesteps per window,” not per-scenario penalty weights.
Spooky — QUBO Mathematical Model · Weight tuning
21

## Slide 22
METHODOLOGY
Current production penalty sets (config/config.yaml)
Penalty | crash (default) | swap
K_hot | 9 | 9
K_adj | 4.8 | 4.8
K_start | 6.5 | 6.5
K_goal | 3 | 3
K_lock | 4 | 4
K_bt | 2.3 | 2.3
K_tp | 1.2 | 1.2
K_goal_approx | 0.7 | 0.7
K_crash | 3 | 2.7
K_swap | — | 3 (kept ≤ K_crash to avoid over-constraint)
“swap” replaces “crash” entirely when active — not summed with it.
Spooky — QUBO Mathematical Model · Weight tuning
22

## Slide 23
06
Binary vs. One-Hot Encoding
Explored on explore/binary-encoding, never merged. A negative result — documented precisely enough that it doesn't need re-deriving.
Spooky — QUBO Mathematical Model · Binary vs. One-Hot Encoding
23

## Slide 24
ENCODING ALTERNATIVE
The theoretical appeal: fewer qubits per cell
One-hot uses N variables per (robot, timestep) — one bit per grid cell / graph node.
Binary needs only B = ⌈log₂N⌉ bits to represent the same N positions — exponentially fewer.
N (cells) | one-hot | binary | binary + exact-match ancilla
4 | 4 | 2 | 6
9 | 9 | 4 | 13
16 | 16 | 4 | 20
25 | 25 | 5 | 30
36 | 36 | 6 | 42
A genuine fix needs an exact-match ancilla per real “from” cell to detect adjacency correctly — always strictly more variables than one-hot (B + N > N). The savings are illusory once adjacency is handled honestly.
Spooky — QUBO Mathematical Model · Binary vs. one-hot
24

## Slide 25
ENCODING ALTERNATIVE
Why it fails: adjacency has no closed form
One-hot's adjacency term reads each bit independently (“is this specific cell active”). Binary needs to read the combination of bits meaningfully differently depending on which real cell they encode — the same shared (2B,2B) coefficient block gets tiled across every one of the N possible “from” cells.
That's a degrees-of-freedom mismatch: only O(B²) = O(log²N) free coefficients must simultaneously satisfy the ranking constraints for all N cells at once.
Proven, not approximated: a max-margin LP fit (scipy linprog, highs) finds the optimal separating margin is exactly 0 for every grid ≥ 3×4, including exact powers of 2. linprog solves this exactly — margin = 0 means provably no separator exists, not “wasn't found.” An SDP relaxation can't do better either: there's no non-convexity here to relax against.
A refinement (staying in place made legal + row/column encoded in disjoint power-of-2 bit fields instead of i·N+j) does produce a real positive margin — but only for small, open grids, and it degrades fast with size and obstacles.
Spooky — QUBO Mathematical Model · Binary vs. one-hot
25

## Slide 26
ENCODING ALTERNATIVE
The refinement's actual reach
Map | baseline margin | candidate margin | viable on
3×3, 0 obstacles | 0.333 (6.7%) | 0.625 (12.5%) | SA + hardware
5×5, 0 obstacles | fails | 0.313 (6.3%) | SA + hardware
5×5, 3 obstacles | fails | 0.033 (0.65%) | SA only
10×10, 0 obstacles | fails | 0.096 (1.9%) | SA + hardware (marginal)
obs10x10_easy / hard | fails | fails | neither
50×50+ | — | not computable | —
obs10x10_easy / obs10x10_hard are the project's actual CLI benchmark maps (named in CLAUDE.md) — the refinement doesn't rescue them. Obstacles hurt disproportionately: a 5×5 grid's margin drops roughly 10× going from 0 to 4 obstacles.
Spooky — QUBO Mathematical Model · Binary vs. one-hot
26

## Slide 27
ENCODING ALTERNATIVE
Verdict
Not usable for real MAPF maps.
A genuine fix would need more variables than one-hot already uses (B + N ancilla-based detector > N), not fewer — the entire premise of switching encodings inverts.
One-hot's own qubit-reduction levers — BFS window pruning, var_limit, robot_window_limits — are proven and already qubit-competitive. That's where further qubit reduction should go instead of a new encoding.
Kept as a documented negative result on explore/binary-encoding, not merged into main (quantum/tests/BINARY_ENCODING_FINDINGS.md) — the boundary is precisely characterized so it doesn't need re-proving if revisited.
If ever revisited: stay-in-place-legal + split-field encoding is worth keeping as a building block, but on its own it doesn't change the verdict.
Spooky — QUBO Mathematical Model · Binary vs. one-hot
27

## Slide 28
07
Beyond Path Planning
Spooky plans paths to goals it's handed. It doesn't decide which robot gets which goal — that's a layer this system doesn't have yet.
Spooky — QUBO Mathematical Model · Beyond Path Planning
28

## Slide 29
CURRENT SCOPE
Where Spooky's responsibility ends
Spooky solves:
given a fixed (start, goal, priority) per robot, produce collision-free, coordinated paths
windowed, multi-robot, grid or graph, three solver backends
Spooky does not decide:
which robot is assigned to which task/goal
goal generation from a mission or work-order queue
re-tasking when a robot finishes, fails, or a new task arrives
This is a deliberate boundary today: robot/framework integration (ROS2, DiMOS) is out of scope per CLAUDE.md and handled by argOS, which calls Spooky as a planning backend. Task allocation sits at the same “above Spooky” layer, just not yet built.
Spooky — QUBO Mathematical Model · Task allocation
29

## Slide 30
PROPOSED DIRECTION
A layer above, not a rewrite
Task / mission layer
assigns goals to robots — Hungarian algorithm, auction-based, or market-based bidding
Spooky path-planning layer (current system)
collision-free trajectories for a fixed (robot, goal) set — unchanged
Robot execution layer
argOS / ROS2 / DiMOS — already out of scope, already exists
Interface contract: the task layer emits (robot_id, goal) pairs; everything below that — windowing, penalties, solver choice — stays exactly as it is today.
Spooky — QUBO Mathematical Model · Task allocation
30

## Slide 31
PROPOSED DIRECTION
Could allocation also become QUBO?
Task allocation is itself a classic assignment problem — the same family (Max-Cut, TSP, job scheduling) the paper already cites as QUBO-friendly in Related Work.
Linear/generalized assignment penalty-encodes cleanly: one-hot-per-robot over available tasks, plus a cost term for assignment quality — structurally close to what this model already does for one-hot-per-cell.
Two integration shapes worth weighing, not committing to yet:
joint QUBO — allocation and path variables in one solve, for small fleets
two-stage QUBO — allocation QUBO's output feeds Spooky's path QUBO, keeping variable count linear as fleet size grows (matches this system's existing linear-scaling story)
Flagged as an open design question for future work, not a scoped commitment.
Spooky — QUBO Mathematical Model · Task allocation
31

## Slide 32
SUMMARY
Where this stands
Proven
Core + extra penalties, empirical tuning discipline, swap-collision approximation in production
Documented negative result
Binary encoding — characterized precisely enough to not need re-deriving
Open
Task-allocation layer above path planning — direction proposed, not built
github.com/JavideuS/Spooky · arXiv:2602.14799